## Slide 1: “Understanding the Speed-Acceleration mathematical relationship through the utilisation of the Wheelspeed and the Longitudinal-G Sensors of racecars”
Ioannis Paraskevas (PhD, CEng, CMath, FHEA)
iparaskevas@theiet.org

## Slide 2: Introduction: Long-G and Lat-G sensors
G force: type of acceleration which causes a perception of force. In motorsports:
■ Long-G force is related to the acceleration / deceleration of a racecar in a straight line.
■ Lat-G force is related to acceleration / deceleration of a racecar when cornering (Left turn or Right turn).
Traction Circle (TC) is a configuration which includes the Long-G and Lat-G forces. The TC is a very useful tool for the Racecar data engineer. Possible applications:
(i) Compare two different drivers in terms of their performance by observing the TC envelopes (curve outline of the TC extreme points). The outer envelope corresponds to the more competent driver who managed to reach higher acceleration values.
(ii) Compare two different racecars driven by the same driver under similar conditions (the outer envelope corresponds to the racecar with the higher acceleration capabilities).
This teaching session will focus on the information that the Long-G sensor conveys and more specifically on estimating the acceleration / deceleration signal of a racecar on a straight line through the wheelspeed sensor and on comparing the ‘estimated’ signal with the ‘actual’ signal which is the output of the Long-G sensor.

## Slide 3: Introduction: Long-G and Lat-G sensors

## Slide 4: Introduction: Importance of the Long-G sensor
The information which the Long-G sensor conveys is particular important for the Racecar Data Engineer.
In case the Long-G sensor fails to operate or has been installed or calibrated poorly and consequently the signal it produces is noisy or inaccurate, it is essential that we are able to obtain information in relation to the Acceleration / Deceleration of the vehicle from an alternative source of information.
This is the ‘estimated’ signal for acceleration obtained via the Wheelspeed sensor.
Furthermore, it is important to mention that an accurate Long-G sensor signal in real time is essential in the navigation of Autonomous vehicles.
Please note that the IMechE Formula Student competition launched the ‘Autonomous Vehicle Competition 2018’

## Slide 5: Aims of the lesson
The aims of today’s lesson are:
To estimate the Acceleration of a racecar through the signal of the Wheelspeed sensor. In other words, relate the Speed and Acceleration quantities for real signals
To compare the estimated Acceleration signal (obtained from the Wheelspeed sensor) with the actual Acceleration signal (obtained through the Long-G sensor)
To appreciate the importance of filtering in applications involving real signals

## Slide 6: Background theory & Revision
Wheelspeed sensor signal: provides the speed of the vehicle
Longitudinal-G (Long-G) sensor signal: provides the acceleration (positive values) and the deceleration (negative values) of a vehicle in a straight line
Mathematical Relationship between Speed and Acceleration:
differentiation
Speed Acceleration

## Slide 7: Background theory & Revision
The data logger, where the sensors of a racecar are connected to, provides the sensor signals in discrete form.
When the signal is in sampled / discrete, rather than analytic form, we use: Numerical Differentiation
A common method in order to numerically differentiate a discrete signal at point is the one-sided (forward difference) approximation:
where has a small numerical value of

## Slide 8: Background theory & Revision
Conventional methods of numerical differentiation would amplify the noise which most real discrete signals convey  a Low Pass Filter (LPF) is required in order to remove the noise component
A common LPF is the Moving-Average (MA) filter. The MA filter could be used for ‘smoothing’ the discrete signal acquired from a sensor
Each output sample of an MA filter is the result of averaging M-samples (span size) of the input discrete signal

## Slide 9: Background theory & Revision
In order to identify which span size of the MA filter provides the closest estimate of the Acceleration signal to the actual Acceleration (output of Long-G sensor) we utilize the Root Mean Squared Error (RMSE)
The RMSE is utilized in order to measure the absolute error between the ‘estimated’ and the ‘actual’ acceleration through the formula:
where, in our case, corresponds to the discrete points of the estimated signal, to the discrete points of the actual signal and to the total number of data points.
The lower the value of the RMSE, the closer the estimated signal is to the actual signal.

## Slide 10: Steps for the Numerical Differentiation of the Wheelspeed signal
Flowchart for the Numerical Differentiation of the Speed sensor
Pre-processing of the Speed signal
Note: It is very important to consider how the size of the span of the MA filter influences the accuracy of the ‘estimated’ Acceleration signal compared to the ‘actual’ Acceleration signal acquired from the Long-G sensor.
Smoothed Speed
Estimated
Acceleration
Speed
MA filter
Num. Dif/tion

## Slide 11: In-class portfolio exercise - Description
The students will be provided with the MATLAB scripts for the:
(a) Numerical Differentiation; one-sided (forward difference) approximation method
(b) Moving Average filter
(c) Root Mean Squared Error (RMSE)
The students are asked to perform the following tasks as part of an exercise for their Portfolio:

## Slide 12: In-class portfolio exercise - Questions
Tasks [Total Marks: 50, Duration: 2 hours]
(i) Incorporate scripts (a), (b) and (c) in the MATLAB code which you have already developed as part of the previous portfolio exercise (Please utilize the previous flowchart). [10 Marks]
(Note: The aim of the previous exercise was to plot the speed and acceleration signals acquired from the Wheelspeed and Long-G sensors, respectively)
(ii) Develop a figure consisting of two subplots. The upper subplot should present the actual Acceleration signal in (acquired from the Long-G sensor) vs. time (in sec) whereas the lower subplot should present the Numerical Differentiation of the Speed sensor signal i.e. estimated Acceleration, in without the utilisation of the MA filter, vs. time (in sec). Compare the two subplots and comment (50 words).
[10 Marks]

## Slide 13: In-class portfolio exercise - Questions
(iii) Repeat the same process as in (ii) however, select different values for the span size of the MA filter and compare visually the estimated acceleration with the actual acceleration. You can incorporate a number of selected plots in order to support your observations. State briefly your observations (50 words).
[15 Marks]
(iv) Compare the ‘estimated’ acceleration and the ‘actual’ acceleration utilising the RMSE for different span sizes of the MA filter. Specifically, conduct a series of experiments with different span sizes and calculate the corresponding RMSE. Plot the results on a graph. Which values of span size are of particular interest and why? State your observations (50 words).
[15 Marks]

## Slide 14: In-class portfolio exercise – Answers / Results – Question (ii)
Flowchart for the Numerical Differentiation of the Speed sensor without utilising the MA filter
Estimated
Acceleration
Speed
Num. Dif/tion

## Slide 15: In-class portfolio exercise – Answers / Results – Question (ii)

## Slide 16: Steps for the Numerical Differentiation of the Wheelspeed signal
Flowchart for the Numerical Differentiation of the Speed sensor utilising the MA filter
Pre-processing of the Speed Signal
Smoothed Speed
Estimated
Acceleration
Speed
MA filter
Num. Dif/tion

## Slide 17: In-class portfolio exercise – Answers / Results – Question (iii)

## Slide 18: In-class portfolio exercise – Answers / Results – Question (iii)

## Slide 19: In-class portfolio exercise – Answers / Results – Question (iii)

## Slide 20: In-class portfolio exercise – Answers / Results – Question (iv)

## Slide 21: In-class portfolio exercise – Summary of Observations
Brief summary of Observations for Tasks (ii), (iii) and (iv)
Conventional Numerical Differentiation amplifies the noise which most real signals (e.g. signal acquired from the wheelspeed sensor) convey thus, a Low Pass Filter (LPF) is necessary.
The size of the span of the MA filter influences the result. It can be visually observed that the span size of the MA filter needs to be within a certain range of values so that the ‘estimated’ acceleration signal has minimum error (RMSE) compared to the ‘actual’ acceleration signal.
In other words, there is a trade-off between reducing the noise of a real signal and the information loss which occurs due to ‘filtering’ (noise reduction).
Following a series of experiments it was observed that the RMSE is minimum when the span size of the MA filter is 11.

## Slide 22: What we learnt during this session
We used Numerical Differentiation in order to demonstrate the relationship between Speed and Acceleration for real signals acquired from racecar sensors.
We applied Numerical Differentiation and Filtering methods to real discrete signals and understood various parameters and constraints imposed in Engineering applications.
We compared the ‘estimated’ with the ‘actual’ signal.

## Slide 23: Preparation for next week
Revise Numerical Integration
During the next two teaching sessions we will continue focusing on the relation between Distance, Speed and Acceleration utilizing Numerical methods for Differentiation and Integration as well as Filtering.
Similar to today’s session, the actual signals will be signals acquired directly from racecar sensors and the estimated signals will be obtained after processing signals from racecar sensors. Moreover, we will investigate whether the same filtering methods are appropriate for all cases of Numerical Differentiation and Integration.
Integration
Speed
Acceleration
Distance
Differentiation
Differentiation
Integration

## Slide 24
Questions?

## Slide 25
Thank you